## Slide 1: YANG models for ACTN & TE Performance Monitoring Telemetry and Network Autonomics draft-lee-teas-actn-pm-telemetry-autonomics-11
Young Lee, Dhruv Dhody, Satish K, Ricard Vilalta, Daniel King, Daniele Ceccarelli

## Slide 2: Overview
YANG data models that support:
Performance Monitoring (PM) Telemetry for TE-Tunnels and VNs to allow customers to subscribe to certain KPI PM data and be notified with the support of YANG PUSH.
    ietf-te-kpi-telemetry
    ietf-actn-te-kpi-telemetry
Network Autonomics for Scaling Intent for TE-tunnels and VNs.
    i.e. setting the exact condition when the tunnel or VN should be scaled in/out
    and the performance parameter on which scaling should be done!

## Slide 3: Yang Model Relationships
TE Tunnel
TE KPI Telemetry
Augments
VN
VN KPI
Telemetry
Augments
TE KPI Telemetry model provides the TE tunnel level performance monitoring.
Augment the TE tunnel State with performance attributes
  Use the notification subscription (YANG PUSH)
Scaling Intent configurations for auto scaling in/out based on the combination of the performance monitored attributes
VN KPI Telemetry model provides the VN level aggregated performance monitoring.
Augment the VN state as well as individual VN-member state with performance attributes.
  Use notification subscription (YANG PUSH)
Scaling Intent configurations at the VN level to reach to the monitored performance KPI

## Slide 4: Status
Presented in IETF 102 and received good support from the floor.
Presented in IETF 103 and received good support from the floor.
packet-loss and delay-variation deleted from the model to stay as generic model.
Added a new section to explain how scaling mechanism works (section 4).

## Slide 5: Illustration of Scaling Mechanism
module: ietf-te-kpi-telemetry
augment /te:te/te:tunnels/te:tunnel:
+-rw te-scaling-intent
| +-rw scale-in-intent
| | +-rw threshold-time? uint32
| | +-rw cooldown-time? uint32
| | +-rw scale-in-operation-type? scaling-criteria-operation
| | +-rw scaling-condition* [performance-type]
| | +-rw performance-type identityref
| | +-rw threshold-value? string
| | +-rw te-telemetry-tunnel-ref? -> /te:te/tunnels/tunnel/name
| +-rw scale-out-intent
| +-rw threshold-time? uint32
| +-rw cooldown-time? uint32
| +-rw scale-out-operation-type? scaling-criteria-operation
| +-rw scaling-condition* [performance-type]
| +-rw performance-type identityref
| +-rw threshold-value? string
| +-rw te-telemetry-tunnel-ref? -> /te:te/tunnels/tunnel/name
Let say the client wants to set the scaling out operation based on two performance-types (e.g., two-way-delay and utilized-bandwidth for a te-tunnel),
it can be done as follows:
Set Threshold-time: 3600 (sec) (duration for which the criteria must hold true)
Set Cooldown-time: 60 (sec) (the duration after a scaling action has been triggered, for which there will be no further operation)
Set AND for the scale-out-operation-type
List 1: Scaling Condition for Two-way-delay
performance type: Two-way-delay
threshold-value: 300 mile-seconds
List 2: Scaling Condition for Utilized bandwidth
performance type: Utilized bandwidth
threshold-value: 300 megabytes
The above two criteria have to meet at the same time to trigger scale-out operation.

## Slide 6: Next Steps
The authors believe this draft has a good base for WG adoption 

## Slide 7: Thanks!