## Slide 1: A Yang Data Model for VN Operation draft-ietf-teas-actn-vn-yang-06
Young Lee, Dhruv Dhody, Daniele Ceccarelli , Igor Bryskin, Bin Yeong Yoon

## Slide 2: VN Yang
VN
Single node in TE Topology
Native TE Topology
abstract topology
Customer
Network
Yang model for Virtual Network (VN) operations
From the point of view of Customer
An abstraction over the TE-Topo and TE-Tunnel
These models are from the point of view of Network
VN is a higher level of abstraction
VN model depends tightly on the topology model!
Use Connectivity Matrices

## Slide 3: Recent Changes
Relationship to 5G
In the context of 5G transport application, 5G Traffic Provisioning Manager (TPM) that provides slicing requirements to the transport networks (i.e., MDSC) can be considered as a type of CNC. The ACTN CMI provides the necessary interface functions between 5G and transport networks in order to facilitate dynamic VN creation and its lifecycle management with proper feedback loop for monitoring.
Updated illustration and interactions for Type 1 and Type 2 VN
Yang Model Changes
ltp leaf inside vn-ap - used reference to TE-TOPO (was te-tp-id and thus was configurable)
added references for the imported Yang Model
Clarified how this model is used along side TE-topo connectivity matrix (pointer to JSON examples)

## Slide 4: Open Issues
VN Members
Qin asked for clarification in the illustration for Lx in VN-Member L1-L2 etc
VN
Current text says Customer End Point
Can be changed to AP?
Can VN member be set from PE to PE without attaching customer facing access also?
Currently VN Members is from a Source to destination AP
RFC 8453 describes AP as a logical identifier shared between the customer and the operator used to identify an access link. And thus this existed between CE and PE.
Possible solutions
Relax the definition of AP
Use of loopback as an AP
Make AP optional
Recursive use of VN model in MPI that starts with PE

## Slide 5: Thanks!

## Slide 6: BACKUP!

## Slide 7: Related Yang Models
TE Topology
TE Tunnel
VN
L3SM
Augmented with underlying TE
L2SM
Augmented with underlying TE
L1CSM
Augmented with underlying TE
Service Models
TE Models

## Slide 8
ietf-vn
AP
VNAP
VN
VN-Member
From
To
Node
connectivity-matrices
underlay
primary-path
path-constraints
Optimizations
computed-path-properties
connectivity-matrix [id]
From
underlay
Primary-path
path-constraints
Optimizations
To
tunnel-termination-points
tunnel
global
Per entry

## Slide 9
VN Yang Model
AP/VNAP
VN
VN-Member
Abstract Topology with a
Single Node
Underlay
For both VN Type 1 or Type 2 VN Yang model rely on a single node in the abstract TE Topology
The abstract node has
  connectivity-matrices
  connectivity-matrix [id]
  The attributes directly under container connectivity-matrices are the default attributes for all connectivity-matrix entries when the per entry corresponding attribute is not specified. When a per entry attribute is specified, it overrides the corresponding attribute directly under the container connectivity-matrices.
Connectivity
Matrix

## Slide 10: VN Type 1
VN 1
  VN-Member 1 L1-L4
  VN-Member 2 L1-L7
  VN-Member 3 L2-L4
  VN-Member 4 L3-L8
  This VN has following properties
    Bandwidth 500
    Optimize by delay
Abstract Topology with a
Single Node
14: L1-L4 | 17: L1-L7
24: L2-L4 | 38: L3-L8
Connectivity
Matrix
Attributes
  connectivity-matrices
  These properties
  are set in TE Topo
VN is seen as edge to edge links (VN-members) setup as tunnels across underlying networks!

## Slide 11: VN Type 2
VN is seems as a topology of virtual nodes and links
To ease mapping between VN Yang Model and TE models, an abstract single node topology is created with VN topology as the underlay!
The same mapping as VN Type 1 is reused.
VN 2
  VN-Member 1: L1-L8 via S3, S67110, S11
    Set via the underlay path in connectivity-matrix[id]
S3
S9
S124
S67110
S5
S8
S11
Abstract Topology with a
Single Node
VN Topology
Underlay
Underlay

## Slide 12: How: Reference to TE Topology Yang Model
Access | AP/ VNAP -> LTP Ltp of type te-types:te-tp-id
Customer’s Virtual Network | VN -> Abstract Node vn-topology-id of type te-types:te-topology-id abstract-node -> /nw:networks/network/node/tet:te-node-id (reference)
Customer Site to Site connection | VN-Member -> Entry in the connectivity matrix of the abstract node connectivity-matrix-id -> /nw:networks/network/node/tet:te/te- node-attributes/connectivity-matrices/connectivity-matrix/id (reference)
All parameters which are can be set as global attributes to VN are set in the connectivity-matrices (such as bandwidth) and an attribute for a particular VN-member is set in the connectivity-matrix [id] (such as explicit path)!
Duplicate parameters in VN Yang model are removed!