## Slide 1: SF Aware TE Topology YANG Model draft-ietf-teas-sf-aware-topo-model-02
Igor Bryskin (Huawei Technologies)
Xufeng Liu (Volta Networks)
Young Lee James Guichard (Huawei Technologies)
Luis Miguel Contreras (Telefonica)
Danielle Ceccarelli (Ericsson)
Jeff Tantsura (apstra Networks)

## Slide 2: Status
This draft merged the use-case draft draft-ietf-teas-use-cases-sf-aware-topo-model into the appendix.
This draft does not model SF/VNF resource abstraction, leaving it ETSI NFV; it just maintains reference to SF/VNF types for future use.

## Slide 3
augment /nw:networks/nw:network/nw:node/tet:te
/tet:tunnel-termination-point:
+--rw service-function
+--rw tunnel-terminations
+--rw tunnel-termination* [id]
+--rw id uint32
+--rw service-function-id? string
+--rw sf-connection-point-id? string
+--rw enabled? boolean
+--rw direction? connectivity-direction
Reference to a network service
or a network function
Reference to a connection point on a network
service or a network function

## Slide 4: Next Steps
The model is ready for YANG doctor’s review.
The draft is ready for WG LC.

## Slide 5: Backup Slides

## Slide 6: Connectivity matrices introduced by the model
SF2SF CM - describes which SFs could be locally inter-connected, and, if yes, in which direction, via which CPs and at what costs
SF2LTP CM - describes how, in which direction and at what costs a given TE node's SFs could be connected to the TE node's LTPs and hence to SFs residing on neighboring TE nodes that are connected to LTPs at the remote ends of corresponding TE links
SF2TTP CM - describes how, in which direction and at what costs a given TE node's SFs could be connected to the TE node's TTPs and hence to SFs residing on other TE nodes on the topology that could be inter-connected with the TE node via TE tunnels terminated by the corresponding TTPs.

## Slide 7: SFs as TE topology elements
Tunnel Termination Point (TTP)
Server Link Termination Point (S-LTP)
Client Link Termination Point (C-LTP)
Link-12
Node-1
TE-Tunnel-1
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
CP01
CP02
SF1
SF3
SF2
CP12
CP32
CP11
CP21
CP33
CP13
CP31
Service Function (SF)

## Slide 8: Modeling considerations
SFs are modeled as opaque objects identified via globally unique SF_IDs
SF_IDs could be used to look up SFs in ETSI defined TOSCA/YANG data stores to understand SF details
Multiple SFs with the same SF_ID could reside on different TE nodes
Each SF has one or more Connection Points (CPs) identified by SF-unique CP_IDs
SFs use CPs to inter-connect with each other, as well as with the hosting TE node’s LTPs and TTPs

## Slide 9: Interconnecting SFs via ETSI VLs
Tunnel Termination Point (TTP)
Server Link Termination Point (S-LTP)
Client Link Termination Point (C-LTP)
Link-12
Node-1
TE-Tunnel-1
TTP-1
TTP-2
LTP-6
LTP-1
LTP-5
LTP-4
LTP-3
LTP-2
CP01
CP02
SF1
SF3
SF2
CP12
CP32
CP11
CP21
CP33
CP13
CP31
VL_1
ETSI Virtual Link (VL)
Service Function (SF)

## Slide 10: Example of SF2LTP CM: Compute Resource aware Topology
Integrated Cross-Stratum resource model: network + DC compute/storage
Compute Node is attached to network TE node. It contains VMs which can be modeled as a Service Function (SF). VM resources (instances, usage, CPU/Memory) can be modeled and integrated with network topology model to facilitate VM migration, dynamic load balancing, etc.
Added is DC Compute model as an example in this version.
10
N1
N2
N4
N3
N5
N6
L12
L21
L23
L32
L24
L42
L43
L34
L36
L63
L14
L41
L15
L51
L54
L56
L156
L65
L165
L45
L1x
L2x
L3x
L6x
L5x
VIRTUAL SWITCH
VM
VM
VM
DC Compute Node
HYPERVISOR
VIRTUAL SWITCH
VM
VM
VM
DC Compute Node
HYPERVISOR
VIRTUAL SWITCH
VM
VM
VM
DC Compute Node
HYPERVISOR