## Slide 1: Traffic Engineering and Service Mapping Yang Model draft-ietf-teas-te-service-mapping-yang-01
Young Lee, Dhruv Dhody, Daniele Ceccarelli, Jeff Tantsura, Giuseppe Fioccola, Qin Wu
TEAS WG @ IETF 104 - Prague

## Slide 2: TE-Service Mapping Model Overview (1)
The role of TE-service Mapping model is to create a mapping relationship between -
    Services – L3SM, L2SM, L1CSM, etc.
    TE topo, TE tunnel and the VN
TE-service mapping model also provides service policy/intent (e.g., VN/Tunnel selection policy, isolation, availability, etc.) for services (via importing ietf-te-service-mapping-types)
This mapping will facilitate a seamless service operation with underlay-TE network visibility and control.
LxSM
TE & Service
Mapping Types
ietf-lxsm-te-service-mapping
VN
TE-topology
TE-tunnel
augment
Import
reference

## Slide 3: TE-Service Mapping Model Overview (2)
Reorganized Map Type (for VN/Tunnel selection policy)
New VN/Tunnel Binding
Customer could request a VPN service with a new VN/Tunnel not shared with other existing services.
VN/Tunnel Sharing
Customer could request a VPN where the tunnels can be shared with other existing VPNs.
VN/Tunnel Modify
This mode allows the modification of the properties of the existing VN/tunnel (e.g., bandwidth) when VN/Tunnel Selection Mode is applied.
Hard Isolation with deterministic characteristics
Hard Isolation
Soft Isolation

## Slide 4: TE-Service Mapping Model Overview (3)
Introduced “Availability” for customer to indicate the level of availability.
  99.9999 %
  99.999 %
  99.99 %
  99.9 %
  99 %
This needs to be translated into network level policies - protection/reroute policies associated with VN/Tunnels.

## Slide 5: Updates since IETF103
The draft was adopted as a WG draft (the name change).
General applicability statement was added (Abstract & Section 5) to widen the scope of the draft:
  Mapping of VPN services with TE models (TE-tunnel, TE-topology) and VN model.
Models updated to align with changes with ACTN-VN model.
  ACTN-VN model has been generalized: ACTN-VN -> VN

## Slide 6: Next Step
Explore if any new service policy/intent should be added.
Mature Yang models to be ready for Yang doctors’ review.

## Slide 7
Thanks.